## Slide 1: COGNITIVE ROBOTICS PROJECT OBJECT GRASPING

## Slide 2: Project requirements
Intel® RealSense™ Depth Camera D435
NVIDIA® Jetson Nano™
Niryo One
Robot Operating System
Notes: Introduction about components and speak about known issues.

## Slide 3
Camera
The only camera used is fixed on the end effector of the arm, making the environment more compact.
Boxes
Once the program has started, the boxes cannot be moved anymore.
Balls
You can add, remove and move the balls between each operating cycle.
Constraints
Notes: Constraits over the aim of the project

## Slide 4: Software design

## Slide 5: TRAJECTORY LISTENER NODE Moving Niryo One.
NIRYO ONE ROS STACK overview

## Slide 6: ROBOT MANAGER NODE Choose how to move.
ROBOT MANAGER command list
Notes: Initialize system with calibration request
Command line interface with all the available commands of the robot
Request routines
Engine routines

## Slide 7: VISION NODE Look around.
RGB VIDEO and POINT CLOUD acquisition
Intel® RealSense™
Stereo Depth Technology
In a similar way to how human vision works, stereo depth is used to provide the distance of a precise point in the visual field.

## Slide 8: VISION NODE Look around.
DEEP NEURAL NETWORK recognition
MobileNet SSD v2 (COCO)
Pre-trained to detect the location of 90 types objects from COCO dataset.
Input size: 300x300
Fine tuning for 8-classes target.
Notes: Screenshot ballls and boxes in eagle eye
RGB | depth

## Slide 9: VISION NODE Look around.
Chart: Ball recognition
| Red | Blue | Green | White
Precision | 0.98 | 0.63 | 0.78 | 0.92
Recall | 0.7 | 0.81 | 0.28 | 0.65
F1 Score | 0.82 | 0.71 | 0.41 | 0.76
Chart: BOXES RECOGNITION
| Red | Blue | Green | White
Precision | 1 | 0.96 | 0.97 | 0.92
Recall | 0.63 | 0.82 | 0.84 | 0.41
F1 Score | 0.77 | 0.88 | 0.9 | 0.57
Chart: Mean values
Precision | 0.895
Recall | 0.6425
F1 Score | 0.7275

## Slide 10: VISION NODE Look around.
DEEP NEURAL NETWORK confusion matrix
Notes: Initialize system with calibration request
Command line interface with all the available commands of the robot
Request routines
Engine routines

## Slide 11: ENGINE NODE Achieve your target.
ENGINE FLOWCHART

## Slide 12
VISUAL VERBOSE NODE Let me show you
what I’m doing.

## Slide 13: PLANNED IMPROVEMENTS
Managing an even more dynamic workspace
Improve the recognition of targets
Speed up the use of Niryo One Python API
… and surely contemplate a new and nicer hardware structure.

## Slide 14: THANKS!
OBJECT GRASPING for Cognitive Robotics
Allegretti Giovanni
Di Prisco Giovanni
Scaldaferri Antonello
Schettini Marco